## Slide 1: Robot Operating System(ROS) Architecture, Communication Flow & Advantages
Prof. Dr.-Ing. Sebastian Schlesinger
Professor of Business Computer Science
Cybersecurity and Embedded Systems Engineering

## Slide 2: Goals of this lecture
After completing this lecture, students will be able to:
Understand the concept of Robot Operating System (ROS)
Explain the architecture of ROS
Describe communication mechanisms in ROS
Identify advantages of ROS architecture in robotic systems

## Slide 3: What is ROS ?
Robot Operating System (ROS)
set of software libraries and tools that help you building robotic applications
open-source
middleware framework
acting as a software layer on top of a host OS (usually Linux).
provides hardware abstraction, device control and inter process communication
designed for research and prototyping
What it is not?
Realtime OS
For production

## Slide 4: Why ROS ?
Global Community
Proven in Use
Shorten Time to Market
Multi-platform
100% Open-source
Commercial Friendly
Industry Support

## Slide 5: ROS1
ROS 1 Versions:
Noetic (Latest & last ROS 1, Ubuntu 20.04)
Melodic (Ubuntu 18.04)
Kinetic (Ubuntu 16.04)
Older: Indigo, Jade, Hydro, etc.
Common Use Cases:
Academic research and education
Simulation with Gazebo
Legacy robotic systems

## Slide 6: ROS2
What is ROS 2?
Next generation ROS built for modern robotics
Based on DDS (Data Distribution Service) for real time, secure, reliable communication
Supports embedded, multi robot and production systems
Common Use Cases:
Physical robots with real time needs
Safety critical and industrial applications
Cross platform deployments (Linux, Windows, macOS)
ROS 2 Versions:
Humble (Latest LTS, Ubuntu 22.04)
Galactic, Foxy (Previous releases)
Rolling (Continuous, non-LTS)

## Slide 7: ROS1 vs. ROS2
Aspect | ROS 1 | ROS 2
Communication | TCPROS/UDPROS | DDS based
Real Time | Not designed for real time | Built in real time support
Discovery | Centralized (ROS Master) | Decentralized (DDS)
Security | Minimal | Encryption & authentication
Cross Platform | Mainly Linux | Linux, Windows, macOS, RTOS
Build System | catkin | colcon + ament
Parameter Server | Centralized | Distributed per node
ROS 2 is not just an update—it’s a re-architecture for modern robotics.

## Slide 8: Architecture of ROS
Master
Nodes
Topics
Messages
Services
Parameter Server

## Slide 9: Architecture of ROS
ROS Master
Acts as a central coordinator
Responsible for
  Registering nodes
  Managing names and namespaces
  Helping nodes discover each other
ROS Master does not handle data transfer
It only establishes connections between nodes

## Slide 10: Architecture of ROS
Nodes
A node is an independent executable program
Each node performs one specific function
Examples:
  Sensor data processing
  Motion control
  Mapping and localization
A complete ROS system is built by combining multiple nodes

## Slide 11: Architecture of ROS
Topics (Publish–Subscribe Communication)
Topics are named channels used for data exchange
Communication model:
  Publisher → sends data
  Subscriber → receives data
Characteristics:
  Asynchronous communication
  Many-to-many connections

## Slide 12: Architecture of ROS
Messages
Messages define the structure of data exchanged between nodes
Standardized data formats ensure compatibility
Examples:
  sensor_msgs/LaserScan
  geometry_msgs/Twist
Messages allow different nodes to understand shared data

## Slide 13: Architecture of ROS
Services
Services use a request–response communication model
One node requests a service, another provides a response
Used for:
  Starting or stopping processes
  Resetting robot position
Services are synchronous and blocking

## Slide 14: Architecture of ROS
Parameter Server
Central storage for configuration parameters
Stores values such as:
  Robot dimensions
  Sensor limits
  Controller parameters
Advantages:
  Parameters can be changed at runtime
  Avoids recompiling code

## Slide 15: ROS Communication Flow
ROS Master is launched
Nodes register with the master
Publishers advertise topics
Subscribers connect to publishers
Data flows directly between nodes
Communication is efficient and scalable

## Slide 16: Advantages of ROS Architecture
Modular and reusable design
Easy debugging and testing
Supports simulation and real hardware
Suitable for multi-robot systems

## Slide 17: Reflection / Exercise
How would you describe the purpose of ROS in modern robotic systems?
How is data exchange realized between different ROS nodes?
Why ROS is not a classical operating system?
In which situations would you prefer topics over services and why?

## Slide 18: ROS Ecosystem – Gazebo & RViz
Gazebo:
Physics based robot simulator
ROS 1: Gazebo Classic (tightly integrated)
ROS 2: Gazebo Ignition (now Simulator) with native ROS 2 support
Used in projects for: Simulation before real world deployment

## Slide 19: ROS Ecosystem – Gazebo & RViz
RViz (ROS Visualization):
3D visualizer for robot data (sensors, models, paths)
ROS 1: RViz
ROS 2: RViz2 (updated version)
Used in projects for: Visualizing LiDAR scans, robot poses, navigation goals

## Slide 20: When to Use Which Version & Tool
Scenario | Recommended ROS | Recommended Tool
University course / lab | ROS 1 Noetic | Gazebo Classic + Rviz
Physical robot with LiDAR | ROS 2 Humble | RViz2 + real sensor
Multi robot system | ROS 2 | Gazebo Simulator
Legacy code migration | ROS 1 → ROS 2 | Bridge (ros1_bridge)
Embedded / real time | ROS 2 | Micro ROS

## Slide 21: Reflection / Exercise
Discussion Questions:
Why would a company choose ROS 2 over ROS 1 for a new product?
What are the risks of using ROS 1 for a safety critical robot?
How does DDS improve multi robot communication compared to ROS 1’s TCPROS?
When would you use Gazebo vs a real robot for testing?

## Slide 22: Reflection / Exercise
Exercise:
Scenario: You are designing a warehouse robot for inventory scanning.
Decide:
  ROS 1 or ROS 2? Why?
  Which tools (Gazebo, RViz, etc) would you use in development?
  How would you test before deployment?
Write a 1-paragraph justification for your choices.

## Slide 23: ROS Filesystem Concepts
ROS uses an organized structure to manage robot software.
Important elements include:
Nodes: Programs performing specific tasks like controlling motors or reading sensors.
Packages: Collections of nodes and configuration files.
Workspaces: Development environments containing packages.
This structure helps developers organize large robotic systems in manageable parts.

## Slide 24: ROS Filesystem Concepts
Every ROS workspace follows a standard structure:
workspace_name/
├── src/ # Your source code (packages live here)
├── build/ # Build artifacts (compiled code, CMake files)
├── install/ # Installed executables and libraries
└── log/ # Build logs and runtime logs

## Slide 25: ROS Filesystem Concepts
Key Files Inside a Package:
package.xml – Package metadata and dependencies (REQUIRED)
CMakeLists.txt – Build instructions for C++ packages
setup.py – Python package configuration (ROS 2)
launch/ – Directory containing launch files
src/ or scripts/ – Where your source code goes
Environment Variable:
ROS_PACKAGE_PATH tells ROS where to look for packages.

## Slide 26: Workspaces in ROS 1 vs ROS 2
A workspace is where developers create and build ROS projects.
ROS 1 Workspace:
A ROS 1 workspace typically contains:
• src – Stores package source code • build – Contains temporary build files • devel – Contains development executables and environment setup
Build tool used: catkin_make
All packages are usually built together.

## Slide 27: Workspaces in ROS 1 vs ROS 2
Creating a ROS 1 Workspace:
mkdir -p ~/catkin_ws/src
cd ~/catkin_ws
catkin_make
source devel/setup.bash

## Slide 28: Workspaces in ROS 1 vs ROS 2
ROS 2 Workspace:
Whereas,ROS 2 uses a slightly different structure:
• src – Contains packages • build – Compilation files • install – Final installed executables • log – Build logs for debugging
Build tool used: colcon build
ROS 2 allows packages to be built independently which improves performance in large projects.

## Slide 29: Workspaces in ROS 1 vs ROS 2
Creating a ROS 2 Workspace:
mkdir -p ~/ros2_ws/src
cd ~/ros2_ws
colcon build
source install/setup.bash

## Slide 30: Workspaces in ROS 1 vs ROS 2
Comparison Table:
Aspect | ROS 1 (catkin) | ROS 2 (colcon)
Build Command | catkin_make | colcon build
Source Location | devel/setup.bash | install/setup.bash
Build System | catkin | colcon + ament
Python Support | via catkin | native (ament_python)
Default Workspace Name | catkin_ws | ros2_ws

## Slide 31: Creating Packages
A package is created to organize related robot software.
When creating a package, developers define:
• Package name
• Dependencies (required libraries or packages)
• Build configuration

## Slide 32: Creating Packages
Inside a package, developers usually add:
Node source code
Launch files
Parameter configurations
Resource files

## Slide 33: Creating Packages
Good package design makes projects modular and reusable.
For example:
One package controls sensors
Another controls robot motion

## Slide 34: Creating Packages
ROS 1 Package:
cd ~/catkin_ws/src
catkin_create_pkg my_pkg rospy std_msgs geometry_msgs
This creates: package.xml, CMakeLists.txt and basic directories.

## Slide 35: Creating Packages
ROS 2 Package:
cd ~/ros2_ws/src
ros2 pkg create my_pkg --build-type ament_python --dependencies rclpy std_msgs
This creates: Full Python package with setup.py, package.xml and module structure.
Available Build Types in ROS 2:
ament_cmake – For C++ packages
ament_python – For Python packages (recommended)
cmake – Legacy CMake style

## Slide 36: Building and Sourcing
After creating packages, they must be built before they can run.
Building:
Compiles code
Links dependencies
Generates executable nodes
If errors occur, they must be fixed before running nodes.

## Slide 37: Building and Sourcing
Building Specific Packages:
# ROS 1: Build only one package
catkin_make --only-pkg-with-deps my_package
# ROS 2: Build selected packages
colcon build --packages-select my_package
# ROS 2: Build with symlinks (for easier Python development)
colcon build --symlink-install

## Slide 38: Building and Sourcing
Sourcing:
Sourcing sets environment variables so ROS can find packages and executables.
It is required:
• After building
• In every new terminal
Without sourcing, ROS cannot locate new packages.
Many developers automatically source workspaces in their terminal configuration.

## Slide 39: Building and Sourcing
Sourcing – The Most Important Step:
# ROS 1 – After every build
source ~/catkin_ws/devel/setup.bash
# ROS 2 – After every build
source ~/ros2_ws/install/setup.bash
# Make it permanent (add to ~/.bashrc)
echo "source ~/ros2_ws/install/setup.bash" >> ~/.bashrc

## Slide 40: Launch Files
Launch files help run multiple ROS nodes automatically.
Instead of manually running many commands, a launch file:
Starts several nodes
Sets parameters
Configures system settings

## Slide 41: Launch Files
Example robot launch:
Start sensors
Start navigation
Start controllers
Start visualization tools
This saves time and avoids mistakes.

## Slide 42: ROS 1 vs ROS 2 Launch Files
ROS 1 launch files are written in XML.
Whereas, ROS 2 launch files are written in Python, allowing more flexibility and logic control

## Slide 43: ROS 1 vs ROS 2 Launch Files
ROS 1 Launch File (XML format) – demo.launch:
<launch>
<node pkg="my_package"
type="my_node.py"
name="my_node"
output="screen"/>
<node pkg="another_package"
type="another_node"
name="another_node"
respawn="true"/>
</launch>

## Slide 44: ROS 1 vs ROS 2 Launch Files
ROS 2 Launch File (Python format) – demo.launch.py:
from launch import LaunchDescription
from launch_ros.actions import Node
def generate_launch_description():
return LaunchDescription([
Node(
package='my_package',
executable='my_node',
name='my_node',
output='screen'
),
Node(
package='another_package',
executable='another_node',
name='another_node',
respawn=True
)
])

## Slide 45: Reflection / Exercise
Discussion Questions:
Why did ROS 2 switch from catkin to colcon?
What are the advantages of Python based launch files?
How does ROS 2's package.xml format improve dependency management?
Why is it important to keep ROS 1 and ROS 2 workspaces separate?

## Slide 46: Reflection / Exercise
Exercise:
Create a ROS 2 package called student_pkg
Add two nodes: a publisher and a subscriber
Create a launch file that starts both nodes
Build your package and test it